## Slide 1
DELIVERABLE 3 · COMPSCI-603
Autonomous Pick-and-Transport
on the DJI RoboMaster EP Core
ROS 2 Humble · camera marker detection · ToF reactive avoidance · arm / gripper actions
Jeet Patel · Linfeng Lyu · Piyush Maheshwari · Shivraj Bhatti
Team intro · COMPSCI-603 GP-D3 · 1 / 12

## Slide 2
Change in plans:
Project framing · COMPSCI-603 GP-D3 · 2 / 12
history
rocket_launch
Before - Triton
Now - DJI EP Core
•ROS 1 Noetic
•RPLIDAR + RealSense + wheel odometry
•GMapping + move_base + TEB planner
•Jetson Nano onboard compute
•Map-first: build a map, then plan
•ROS 2 Humble, off-board laptop / VM
•RGB camera + ToF sensor
•Marker-based visual servoing
•Arm and gripper via action servers
•No LiDAR → local cues + FSM instead
Key consequence: no 2-D LiDAR means no SLAM pipeline, the robot reacts to what it sees (markers, ToF distance) rather than occupancy map.

## Slide 3
HARDWARE
DJI RoboMaster EP Core
Compute runs off-board over Wi-Fi; the robot handles low-level execution.
hardware · COMPSCI-603 GP-D3 · 3 / 12
RGB camera
/camera/image_color
marker detection and visual servoing
ToF sensor
/range_0
forward distance - emergency stop trigger
Omnidirectional chassis
/cmd_vel (x / y / yaw)
holonomic drive - no turning in place needed
Arm + gripper
MoveArm / GripperControl actions
pick, carry, and place sequences
Off-board laptop
ROS 2 Humble + robomaster_ros driver
all high-level logic runs here over AP mode

## Slide 4
ARCHITECTURE
ROS 2 node graph: perception feeds task controller
Architecture · COMPSCI-603 GP-D3 · 4 / 12
RoboMaster driver
robomaster_ros
Perception
vision.py: ArUco (solvePnP) · people_avoidance.py: person tracking
Safety
obstacle.py + people_avoidance.py · ToF threshold + bypass states
State machine
main.py · Search → Approach → Pick → Navigate → Avoid → Place
Actuation
chassis_control.py + arm_control.py · /cmd_vel + action servers
Source modules
main.py
vision.py
obstacle.py
chassis_control.py
arm_control.py
people_avoidance.py

## Slide 5
PERCEPTION
Camera frames → task cues
Marker identity tells the state machine what goal it sees; geometry drives approach / alignment.
Perception · COMPSCI-603 GP-D3 · 5 / 12
Detect
OpenCV ArUco or RoboMaster /vision
Estimate
Marker center, area, pose / distance
Publish
markers · people annotated image
Consume
FSM selects target and drive speed
Marker assignments
ID 0
Object / pickup target
IDs 1–4
Waypoints (in order)
ID 10
Destination

## Slide 6
REACTIVE SAFETY
ToF-triggered avoidance
Safety overrides visual navigation when the forward distance drops below threshold.
ToF + avoidance · COMPSCI-603 GP-D3 · 6 / 12
Classification
Person-motion states: UNKNOWN, MOVING, STATIONARY
Center-velocity tracker from detection package
State gates which bypass action to take
Emergency layer
ToF /range_0 has hard priority over visual navigation
Drops below 0.50 m → blocked; clears above 0.80 m
Chassis stops; 3-nudge forward recovery before giving up
Recovery
Strafe left or right to clear obstacle
Bypass timer + cooldown prevent thrash
Forward nudge checks clearance
Resume saved FSM state on clear

## Slide 7
BEHAVIOR LAYER
Task Finite-state machine diagram
FSM · COMPSCI-603 GP-D3 · 7 / 12

## Slide 8
MANIPULATION
Arm + gripper: pick, carry, place
pick_up(): open → lower (x=0.15m, z=0.10m) → close → lift (x=0.09m, z=0.07m). place_down(): lower (x=0.18m, z=0.05m) → open → retract (x=0.09m, z=0.10m).
Manipulation · COMPSCI-603 GP-D3 · 8 / 12
1. ALIGN
Center on object marker before initiating pick or place.
Visual servo adjusts x / y / yaw.
2. GRASP
MoveArm moves to pick pose.
GripperControl closes on object.
3. CARRY
Arm retracts to safe carry height.
FSM transitions to NAVIGATE for waypoint following.
4. PLACE
Approach destination marker, servo to alignment.
Arm extends, gripper releases, robot backs away.

## Slide 9
STATUS
Implementation snapshot
Core modules are done; physical tuning and repeatable eval runs remain.
Team / current status · COMPSCI-603 GP-D3 · 9 / 12
Completed ✓
ROS 2 Humble + robomaster_ros driver build path
ArUco / marker perception pipeline (vision.py)
Person tracking + EMA velocity classifier (people_avoidance.py)
ToF obstacle module + debounce logic (obstacle.py)
Chassis command module (chassis_control.py)
Arm / gripper action sequences (arm_control.py)
End-to-end FSM (main.py) with state-memory fix
In progress
Physical integration: repeatable runs with markers + obstacles
Tuning pick / place marker distances and alignment thresholds
Validating ToF false-positive rate on the real floor
Recording final demo trials for evaluation table

## Slide 10
EVALUATION
Trackable metrics
Evaluation · COMPSCI-603 GP-D3 · 10 / 12
Task success rate
% of trials completing pick → waypoints → place without reset
Collision / E-stop count
Physical contacts and emergency stops per run
Completion time
Full circuit time compared to clean baseline
Marker detection rate
Detection reliability under varied lighting and angles
Avoidance recovery rate
Successful ToF bypass events / total obstacle encounters
Manual interventions
Operator resets required per trial
Test cases: clear path · static obstacle · person crossing · marker temporarily lost · pick / place alignment variation

## Slide 11
TEAM
Workload split
All members · COMPSCI-603 GP-D3 · 11 / 12
Jeet Patel
VLA / action-generation framing
Command smoothing and control interface
25%
Linfeng Lyu
Visual marker / perception pipeline/arm / gripper
Camera detections and target pose
25%
Piyush Maheshwari
RoboMaster hardware integration
ToF obstacle processing and avoidance
25%
Shivraj Bhatti
FSM, TF / control logic
Experiments, metrics, final demo coord.
25%

## Slide 12
Perceive
ArUco markers + ToF distance checks
Sensing the environment through visual markers and time-of-flight sensors.
TAKEAWAY
Decide
Explicit FSM + safety state overrides
Processing sensor data through a Finite State Machine with safety logic.
Local-reactive autonomy for manipulation robot
Act
Chassis velocity + arm / gripper actions
Executing physical movements and manipulation tasks on hardware.
Visible markers, ToF safety, and explicit task states to complete a physical pick-and-transport workflow on real hardware.
Q & A
Team close · COMPSCI-603 GP-D3 · 12 / 12